## Slide 1: LAB 03 Parallel Programming on PULP
Alberto Dequino (alberto.dequino@unibo.it)
Călin Diaconu (calin.diaconu2@unibo.it)
Francesco Conti
Giuseppe Tagliavini

## Slide 2: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks

## Slide 3: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
?

## Slide 4: PULP: A Parallel Ultra-Low-Power Computing Platform
Shared Memory
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
RISC-V
RISC-V
RISC-V
RISC-V
Target a Shared-Memory parallel programming model: 4—16 DSP cores accessing a Shared L1 Memory (Tightly Coupled Data Mem or TCDM)
How is memory organized to allow this?

## Slide 5: PULP: A Parallel Ultra-Low-Power Computing Platform
Shared Memory
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
RISC-V
RISC-V
RISC-V
RISC-V
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
Target a Shared-Memory parallel programming model: 4—16 DSP cores accessing a Shared L1 Memory (Tightly Coupled Data Mem or TCDM)
How is memory organized to allow this?
The memory is organized in Multiple Banks → concurrent access.

## Slide 6: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
TCDM Logarithmic Interconnect
RISC-V
RISC-V
RISC-V
RISC-V
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
Target a Shared-Memory parallel programming model: 4—16 DSP cores accessing a Shared L1 Memory (Tightly Coupled Data Mem or TCDM)
How is memory organized to allow this?
The memory is organized in Multiple Banks → concurrent access.
Solution: full connectivity with 1-cycle latency crossbar

## Slide 7: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
TCDM Logarithmic Interconnect
RISC-V
RISC-V
RISC-V
RISC-V
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
I$
I$
I$
I$
Multiple separate instruction streams (hardware threads): MIMD (Multiple Instruction Multiple Data) execution scheme...

## Slide 8: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
TCDM Logarithmic Interconnect
RISC-V
RISC-V
RISC-V
RISC-V
Shared
Instruction Cache
L0
L0
L0
L0
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
Multiple separate instruction streams (hardware threads): MIMD (Multiple Instruction Multiple Data) execution scheme... but optimized for a single parallel program (SPMD)

## Slide 9: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
TCDM Logarithmic Interconnect
RISC-V
RISC-V
RISC-V
RISC-V
Shared
Instruction Cache
L0
L0
L0
L0
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
High-speed synchronization to minimize overhead in
synchronization primitives

## Slide 10: PULP: A Parallel Ultra-Low-Power Computing Platform
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
RISC-V
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
Data AXI Bus
TCDM Logarithmic Interconnect
DMA
Instruction AXI Bus
RISC-V
RISC-V
RISC-V
RISC-V
Shared
Instruction Cache
L0
L0
L0
L0
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
Data movement is fully software-managed

## Slide 11: PULP Execution Model
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
Data AXI Bus
TCDM Logarithmic Interconnect
DMA
Instruction AXI Bus
RISC-V
RISC-V
RISC-V
RISC-V
Shared
Instruction Cache
L0
L0
L0
L0
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
Fabric Controller
Thread
The Cluster is clock-gated at boot: a single thread runs on the Fabric Controller (MCU core)

## Slide 12: PULP Execution Model
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
Data AXI Bus
TCDM Logarithmic Interconnect
DMA
Instruction AXI Bus
RISC-V
RISC-V
RISC-V
Shared
Instruction Cache
L0
L0
L0
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
Fabric Controller
Thread
Activate the cluster and call a function on the cluster core 0
Core 0
Thread

## Slide 13: PULP Execution Model
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
Data AXI Bus
TCDM Logarithmic Interconnect
DMA
Instruction AXI Bus
Shared
Instruction Cache
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
Fabric Controller
Thread
Fork an execution team on multiple cluster cores; they can be synchronized with barriers and critical sections
Core 0
Thread

## Slide 14: PULP Execution Model
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
Data AXI Bus
TCDM Logarithmic Interconnect
DMA
Instruction AXI Bus
Shared
Instruction Cache
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
Fabric Controller
Thread
All code is in L2 memory (cached for cluster threads)
Core 0
Thread

## Slide 15: PULP Execution Model
APB
CLK
TIMER
DEBUG
SPI M
CAMIF
I2C
UART
µDMA
DEBUG
ROM
Logarithmic Interconnect
APB
GPIO
I2S
SDIO
EVENT
SoC CTRL
INTC
ACCEL
Pad Control
L2
Bank
L2
Bank
L2
Bank
L2
Bank
Interleaved banks
L2
Bank
L2
Bank
private banks
Data AXI Bus
TCDM Logarithmic Interconnect
DMA
Instruction AXI Bus
Shared
Instruction Cache
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
HW Synch
Fabric Controller
Thread
Stacks are in L2 for the FC, and in L1 (TCDM) for the cluster cores (not cached!)
Core 0
Thread

## Slide 16: PULP Microcontroller Software Interface Standard (PMSIS)
RTOS (freertos, pulpos, zephyr)
Application
Native OS features
(threading, ...)
PMSIS Drivers
hyperbus, UART, DMA, cluster ...
Chip features
(SPI, DMA, PMU ...)
PMSIS BSP
hyperram, hyperflash
Device features
(camera ...)

## Slide 17: PMSIS: How to Manage a Device Lifecycle
Configuration and initialization (device specific) conf_init() open_from_conf()
Prepare the device for usage: open()
Perform required operations (device specific)
Release the resources close()

## Slide 18: PMSIS: Using the Cluster as a Device
struct pi_device cluster_dev = {0};
struct pi_cluster_conf conf;
struct pi_cluster_task cluster_task = {0};
// task allocation
pi_cluster_task(&cluster_task, cluster_entry, NULL);
// init the cluster
pi_cluster_conf_init(&conf);
pi_open_from_conf(&cluster_dev, &conf);
// open the cluster
if (pi_cluster_open(&cluster_dev)) return -1;
// offload an entry point to the cluster
pi_cluster_send_task_to_cl(&cluster_dev, &cluster_task);
// releasing the cluster
pi_cluster_close(&cluster_dev);
PMSIS data structures
Create a task for the cluster
Initialize the cluster device
Open the cluster device
Execute code on the cluster
Release the cluster device
Function pointer

## Slide 19: Executing on the Cluster: Fork/join + SPMD
static void cluster_entry(void *arg)
{
printf("Hello from cluster\n");
// ...
pi_cl_team_fork(NUM_CORES, cluster_fn, (void *) &args);
// ...
}
Executed on core 0
Fork the execution of the same function on NUM_CORES cores
Executed on core 0
Function pointer
Data pointer

## Slide 20: Synchronization: Barriers and Critical Sections
Barriers (used for intermediate and final join points): pi_cl_team_barrier();
Critical sections (used to avoid critical races): pi_cl_team_critical_enter(); // code in the critical section pi_cl_team_critical_exit();

## Slide 21: Hands-on Part, LAB 01 Recap: Getting Started: Docker setup
How to install:
  Install Docker Desktop* - https://www.docker.com/products/docker-desktop/
*For Windows users, it’s recommended to use it through Windows Subsystem for Linux - WSL (install instructions); otherwise, it would become quite computationally-intensive, since it runs through a virtual machine.
  Install VS Code https://code.visualstudio.com/
  In VS Code, install the Dev Containers extension: https://marketplace.visualstudio.com/items?itemName=ms-vscode-remote.remote-containers

## Slide 22: Hands-on Part, LAB 01 Recap: Getting Started: Open project in the Docker container
$ git clone https://github.com/EEESlab/HSDES-LAB04-PULP_Parallel_Bare.git
*In these labs we will always use Git. It is a popular tool, so a useful skill to have. Here is a good intro tutorial.
First steps:
1. Clone* this lab’s project locally (in WSL, if using it)
At this moment, the project is open in your local “environment”.
We need to open it in the Docker container. For this, in VS Code:
1. Press CTRL+Shift+P (open command palette)
2. Type in “Dev Containers: Reopen in Container” and press Enter
We are now inside the container. From now on, when opening VS Code,
the project will automatically open inside the Docker container.
* We will also need to use the terminal from VS Code (CTRL+Shift+`) from now on,
since it is the one accessing inside the running container!
2. Enter the newly created local directory of the project
3. Open the project in VS Code
$ cd HSDES-LAB04-PULP_Parallel_Bare
$ code .

## Slide 23: Exercise 01: Vector Addition
Now, take a look at the code and run the function on the cluster!
$ cd 01_vectAddPar
$ make clean all run CORES=1
How many clock cycles does it take SINGLE core ?

## Slide 24: Ex. 01 - Method #1
void vectAddPar(int * pSrcA, int * pSrcB, int * pDstC, int n) {
int i, core_id;
core_id = pi_core_id();
for (i = core_id; i < n; i += NUM_CORES) {
pDstC[i] = pSrcA[i] + pSrcB[i];
}
pi_cl_team_barrier();
}
With NUM_CORES == 4 and n == 16:
Iterations:
Core id:
Distribute single iterations among the available cores
Stop the execution once all cores have reached this point
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3
01_vectAddPar/kernels.c

## Slide 25: Ex. 01 - Method #2 - balanced workload
void vectAddPar(int * pSrcA, int * pSrcB, int * pDstC, int n) {
int i, core_id, i_start, i_end, i_block, i_chunck;
core_id = pi_core_id();
i_chunk = n / NUM_CORES;
i_start = core_id * i_chunk;
i_end = i_start + i_chunk;
for (i = i_start; i < i_end; i++) {
pDstC[i] = pSrcA[i] + pSrcB[i];
}
pi_cl_team_barrier();
}
With NUM_CORES == 4 and n == 16:
Iterations:
Core id:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3
Split the wokload into adjacent blocks (chunks) and compute their bounds [i_start, i_end)
01_vectAddPar/kernels.c

## Slide 26: Ex. 01 - Method #2 - generic workload
void vectAddPar(int * pSrcA, int * pSrcB, int * pDstC, int n) {
uint32_t i, core_id, i_chunk, i_start, i_end, i_block;
core_id = pi_core_id();
i_chunk = (n + NUM_CORES – 1) / NUM_CORES;
i_start = core_id * i_chunk;
i_end = i_start + i_chunk < n? i_start + i_chunk : n;
for (i = i_start; i < i_end; i++) {
pDstC[i] = pSrcA[i] + pSrcB[i];
}
pi_cl_team_barrier();
}
With NUM_CORES == 4 and n == 18:
Iterations:
Core id:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3
Integer division with rounding towards infinity (1)
Check the upper bound of the iteration space
(1)
01_vectAddPar/kernels.c

## Slide 27: Ex. 01 - Parallel Vector Add - Try on your own
Apply the parallelization strategies by adapting the vectAddPar function.
Run the code with different values of CORES = {2, 4, 8}
Make sure the checksum output is correct.
Measure the number of clock cycles and compute the parallel speedup=
$ make clean all run CORES=2
$ make clean all run CORES=4
$ make clean all run CORES=8

## Slide 28: Exercise 02 - Parallelize a Matrix Multiplication Kernel
This example is a “template” containing the code to run a matrix multiplication on the cluster. However, this is not optimized:
Your task is to parallelize the code, using methods similar to the previous exercise.
Measure the speed up and collect the performance statistics!
Is the speed up ideal? If not, why?
$ cd ../02_matrixMulPar
$ make clean all run CORES=1

## Slide 29: Exercise 03: Parallelize an algorithm with data dependencies
Create a new application using the previous exercises as templates, and rename it “03_computePi”
Test the sequential code and print the result! float iterative_pi(int n) { float x, area=0.0f; int i; for(i=0; i<n; i++) { x = (i + 0.5f)/n; area += 4.0f/(1.0f + x*x); } return area/n; }
Parallelize the iterative_pi kernel. *Hint: Make use of the critical section to update the area variable!

## Slide 30: *References on Makefile rules
The Makefile is a “recipe” used to call the compiler/linker and, in this case, also to run the program. You can also chain several rules (e.g., make clean all run) and pass options (e.g., runner_args="--vcd")
Remove any existing build
make clean
Build program (calling compiler + linker)
make all
Run the program
make run
Run options: you can change them by adding runner_args="OPTIONS"
make run runner_args="--trace=.*insn.*" > trace.log # written trace of instructions
Disassembling:
# Disassemble without inlined source code:
make dis > test.S
# Disassemble with inlined source code:
/pulp/pkg/pulp_riscv_gcc/bin/riscv32-unkown-elf-objdump –D -S > test.S

## Slide 31
Alberto Dequino – alberto.dequino@unibo.it
Călin Diaconu – calin.diaconu2@unibo.it