## Slide 1: LAB01 - Embedded Programming on PULP
Alberto Dequino (alberto.dequino@unibo.it)
Calin Diaconu(calin.diaconu2@unibo.it)
Francesco Conti
Giuseppe Tagliavini

## Slide 2: Labs (tentative) schedule
LAB1 | Fri. 13/03 | 3h | Embedding Programming on PULP – I
LAB2 | Fri. 10/04 | 3h | Embedding Programming on PULP - II
LAB3 | Fri. 15/05 | 3h | Digital Signal Processing on MCUs
LAB4 | Fri. 22/05 | 3h | Bare-metal parallelization on PULP
LAB5 | Fri. 29/05 | 3h | OpenMP parallelization on PULP + Parallel DSP Computation

## Slide 3: Goal of the Class
Intro to the PULP platform and the PULP-SDK
Some basics of C programming on PULP
Measuring Performance and Assembler
The class is meant to be interactive: code together and on your own!
Now…
Open your container with the PULP-SDK installed

## Slide 4: Get confident with the PULP Platform
1 + 8 high-performance cores: extended RISC-V ISA
On-chip Memories
  A level 2 Memory for all the cores
  A level 1 Memory shared by all the cores in Cluster
A multi-channel 1D/2D cluster-DMA controls the transactions between the L2 Memory and L1 Memory
A smart, lightweight and completely autonomous DMA (micro-DMA) capable of handling complex I/O scheme
  HyperBus, I2S, CPI, timers, SPI, GPIOs, etc…
GitHub HW Project: https://github.com/pulp-platform/pulp
HW Documentation: https://raw.githubusercontent.com/pulp-platform/pulp/master/doc/datasheet.pdf

## Slide 5: Getting Started: Docker setup
How to install:
  Install Docker Desktop* - https://www.docker.com/products/docker-desktop/
  *For Windows users, it’s recommended to use it through Windows Subsystem for Linux - WSL (install instructions); otherwise, it would become quite computationally-intensive, since it runs through a virtual machine.
  Install VS Code https://code.visualstudio.com/
  In VS Code, install the Dev Containers extension: https://marketplace.visualstudio.com/items?itemName=ms-vscode-remote.remote-containers

## Slide 6: Getting Started: Open project in the Docker container
$ git clone https://github.com/EEESlab/HSDES-LAB01-PULP_Embedded_Programming.git
$ cd HSDES-LAB01-PULP_Embedded_Programming
$ code .
*In these labs we will always use Git. It is widely used, so a good skill to have. Here is a good intro tutorial.
First steps:
1. Clone* this lab’s project locally (in WSL, if using it)
2. Enter the newly created local directory of the project
3. Open the project in VS Code
At this moment, the project is open in your local “environment”.
We need to open it in the Docker container. For this, in VS Code:
1. Press CTRL+Shift+P (open command palette)
2. Type in “Dev Containers: Reopen in Container” and press Enter
We are now inside the container. From now on, when opening VS Code,
the project will automatically open inside the Docker Container.

## Slide 7: Getting Started: Helloworld
From now on, we need to work through
VS Code, since now it’s the Docker container’s
access point. Now, we need to open a terminal
inside the container, also through VS Code.
Access it like in the image on the right,
through the top-left task bar.
The terminal will open in the bottom part of
the window.
Now we are ready to run the “Hello , world” example. Use the commands below:
$ cd pulp-helloworld
$ make clean all run
If everything went well, you will now see the “Helloworld from PULP!” message in the terminal.

## Slide 8: Behind the scenes: Build Automation with Makefiles
Build automation is the process of automating the main steps required to create a software, including compiling, assembling, linking and testing
Make is one of the most widespread utilities
configuration files are called Makefiles
A Makefile contains rules in the form: target: prerequisites <TAB> command
$ make clean all run
Clean previous build processes ( folder BUILD/ )
Compile the program and produce the binary code
Run the binary code on the target platform
APP = test
# This is a comment
APP_SRCS += test.c
APP_CFLAGS += -O3 -g
APP_LDFLAGS +=
include $(RULES_DIR)/pmsis_rules.mk
Makefile

## Slide 9: Compilation toolchain
A compilation toolchain includes several tools to achieve its final goal
The COMPILER translates high-level source code (e.g., C) to a lower-level representation (e.g., assembly)
The ASSEMBLER is a program that translates assembly language to machine language
The LINKER combines multiple object files into a single executable
file1.c
file2.c
file1.s
file2.s
Assembler
file1.o
file2.o
libxyz.a
Compiler
Linker
executable
program
file1.c
file2.c
Source code
Assembly
Object files
User libraries
+
System libraries
A cross compiler creates binary code for a platform different from the one on which it is running
Typically used to compile code for embedded platforms on a development host (e.g., PULP)
Cross compiler for PULP: build == host == x86_64-linux target = riscv-none

## Slide 10: PULP Software Environment Workflow
Compiling
Code
PMSIS
Board
RTL Platform
Executing
Multiple Targets
Virtual Platform
Simulator (GVSOC)
Default
Application code: main function, application libraries, e.g. CNN inference function code…
Runtime SW: Peripheral Drivers, API, Board support packages (BSP)
PULP Microcontoller Software Interface Standard (PMSIS) layer
GCC-RISCV compiler

## Slide 11: PULP Software Environment Workflow
SoC Model
Configuration Files
Generators
GVSOC
Compiling
Code
PMSIS
Board
RTL Platform
Executing
Multiple Targets
Virtual Platform
Simulator (GVSOC)
Default
Building the GVSOC simulator
PULP-SDK

## Slide 12: PULP SDK
The PULP-SDK (https://github.com/pulp-platform/pulp-sdk ) includes a PULP platform simulator (GVSOC) and the SW libraries.
Check the /pulp/pulp-sdk folder:
rtos/ runtime code and software stack
tools/ configuration files, python generators, pulp runner and the gvsoc components
tests/ sample code to test the platform’s features
applications/ full-application codes
$ git pull origin main
$ source configs/pulp-open.sh
$ make build
You could get the latest update from the open-source community and rebuild the GVSOC simulator
DON’T do it
$ cd /pulp/pulp-sdk

## Slide 13: GVSoC – Features
Virtual platform features:
  C++ for fast native simulation
  Python for instantiation + configuration
  Complete set of traces to see what happens
Timing model:
  Fully-event based (cycle-accurate), instances can generate events at specific time
  Includes timing models for interconnects, DMACs, memories…
  Performance counters for information on the execution
Simulation performance:
  Around 1 Million Instructions Per Second (MIPS)
  Functionally aligned and calibrated with HW
  Timing accuracy is within 10-20% of target HW

## Slide 14: Example I: Sum values of a Vector on the PULP platform
The vector_sum() function returns the element-wise add of the values in array_1[N]
main includes the function testbench
UART
I2C
CPI
SPI
HyperBus
GPIO
Micro DMA
L2
Memory
512kB
FC
Core
DMA
L1 Cluster TCDM
Mem
64kB
Core
0
Core
1
Core
2
Core
3
Core
5
Core
6
Core
7
Core
8
Octa Core Cluster Domain
Microcontroller Domain
$ cd vector_sum/
$ make clean all run
Output: Result is correct
Good practice for testing!
OFF
Fabric Controller (FC) Core runs the program
Array_1
binary
Now take a look at the code.
What happens if you change:
(line 13) #define N 350
How would you solve it?
Try on your own!
  Array initialization (a[i] = i)
  Function call
  Check result

## Slide 15: Casting Variables and Passing Parameters via Makefile
(line 13) #define N 350
Output: Result is not correct. Got 37105 instead of 61425
1 2 3 4 5 6 7 8 9 10 11 12 13 14 [….] 247 248 249 250 251 252 253 254 255 0 1 2 3 4 5 6 7 8 […] 88 89 90 91 92 93 94
If printing the array_1 values after initialization:
unsigned char datatype can represent numbers from 0 to 255!! If >255, assigned values get truncated (value % 256)!
Solution: cast array_1 to int or short int (and the function’s arguments!)
APP = test
N?=50
APP_SRCS += test.c
APP_CFLAGS += -O3 –g
APP_CFLAGS += -DN=$(N)
APP_LDFLAGS +=
include $(RULES_DIR)/pmsis_rules.mk
Makefile
After applying the fix, comment line 13, change the Makefile and launch:
$ make clean all run N=350

## Slide 16: Try on your own: Find an element within an array
Design a function that returns the index of a given element (element_to_find) within an array A_ar
  int find_element(int * A_ar, int size, int element_to_find)
  What is it returned if the element_to_find is not present in the array?
  What if multiple value of the array correspond to element_to_find ?
$ cd array-find-element
$ make clean all run
Which index corresponds to element_to_find=11 ?
0 | 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17
array[N]
return = 6

## Slide 17: Example II: Matrix-Vector Product
N
X
M
M
=
N
$ cd matrix_vector/
$ make clean all run

## Slide 18: Example II: Matrix-Vector Product
A multi-dimensional array (e.g., a matrix) is stored in its flattened form.
N
M
M*2
M*1
0
0+2
M*1+2
M*2+2
0+2
M*1+2
M*2+2
In general: Mat[i][j] -> M[i*M+j]
$ cd matrix_vector/
$ make clean all run
r0
r1
r2
r0
r1
r2

## Slide 19: Example II: Matrix-Vector Product
// generic matrix-vector multiplication
int gemv(int N, int M, float * mat, float *vec, float * output_vec){
for (int i=0; i<N; i++){
for (int j=0; j<M; j++){
vec_o[i] += mat_i[i*size_M+j] * vec_i[j];
}
}
}
N :i
X
M :j
M
=
N

## Slide 20: Assembly Code
A disassembler is a computer program that translates machine language into assembly language—the inverse operation to that of an assembler. Disassembly, the output of a disassembler, is often formatted for human-readability rather than suitability for input to an assembler, making it principally a reverse-engineering tool. [Wikipedia]
$ make dis > dis.txt
To produce the assembly code, use the command:
Check the RI5CY User manual: https://riscv.org/wp-content/uploads/2017/05/riscv-spec-v2.2.pdf https://www.pulp-platform.org/docs/ri5cy_user_manual.pdf

## Slide 21: Assembly Code
1c008706 <gemv>:
1c008706: 02a05d63 blez a0,1c008740 <gemv+0x3a>
1c00870a: 00259f13 slli t5,a1,0x2
1c00870e: 8fb6 mv t6,a3
1c008710: 01e68e33 add t3,a3,t5
1c008714: 4e81 li t4,0
1c008716: a005 j 1c008736 <gemv+0x30>
1c008718: 0048230b p.lw t1,4(a6!)
1c00871c: 0046a88b p.lw a7,4(a3!)
1c008720: 431c lw a5,0(a4)
1c008722: 431307b3 p.mac a5,t1,a7
1c008726: c31c sw a5,0(a4)
1c008728: ffc698e3 bne a3,t3,1c008718 <gemv+0x12>
1c00872c: 0e85 addi t4,t4,1
1c00872e: 967a add a2,a2,t5
1c008730: 0711 addi a4,a4,4
1c008732: 01d50763 beq a0,t4,1c008740 <gemv+0x3a>
1c008736: 86fe mv a3,t6
1c008738: 8832 mv a6,a2
1c00873a: fcb04fe3 bgtz a1,1c008718 <gemv+0x12>
1c00873e: b7fd j 1c00872c <gemv+0x26>
1c008740: 8082 ret
PC
opcode
Instruction
1c008738: 8832 mv a6,a2
// generic matrix-vector multiplication
void gemv(int size_N, int size_M,
float * mat_I, float *vec_i, float * vec_o)
{
for (int i=0; i<size_N; i++){
for (int j=0; j<size_M; j++){
// mulitply accumulate operation
vec_o[i] += mat_i[i*size_M+j] * vec_i[j];
}
}
}
Inner loop
In the Makefile:
Change from -03 to -01. What has changed in the assembly?
Remove –mnohwloop. What has changed in the assembly?

## Slide 22: Assembly Code: O3 optimization
1c008706 <gemv>:
1c008706: 02a05c63 blez a0,1c00873e <gemv+0x38>
1c00870a: 02b05a63 blez a1,1c00873e <gemv+0x38>
1c00870e: 00259e93 slli t4,a1,0x2
1c008712: 050a slli a0,a0,0x2
1c008714: 00a70e33 add t3,a4,a0
1c008718: 01d68333 add t1,a3,t4
1c00871c: 0047258b p.lw a1,4(a4!) # 10004 <__l1_heap_size+0x20>
1c008720: 87b6 mv a5,a3
1c008722: 8532 mv a0,a2
1c008724: 0045288b p.lw a7,4(a0!)
1c008728: 0047a80b p.lw a6,4(a5!)
1c00872c: 430885b3 p.mac a1,a7,a6
1c008730: feb72e23 sw a1,-4(a4)
1c008734: fef318e3 bne t1,a5,1c008724 <gemv+0x1e>
1c008738: 9676 add a2,a2,t4
1c00873a: feee11e3 bne t3,a4,1c00871c <gemv+0x16>
1c00873e: 8082 ret
// generic matrix-vector multiplication
void gemv(int size_N, int size_M,
float * mat_I, float *vec_i, float * vec_o)
{
for (int i=0; i<size_N; i++){
for (int j=0; j<size_M; j++){
// mulitply accumulate operation
vec_o[i] += mat_i[i*size_M+j] * vec_i[j];
}
}
}
APP = matrix-vector
APP_SRCS += test.c
APP_CFLAGS += -O3 -g -mnohwloops
APP_LDFLAGS +=
include $(RULES_DIR)/pmsis_rules.mk
Inner loop
The -03 optimized code get rid of a lw instruction because the accumulator is kept in the register file!

## Slide 23: Assembly Code: HW loops
1c008706 <gemv>:
1c008706: 04a05463 blez a0,1c00874e <gemv+0x48>
1c00870a: 04b05263 blez a1,1c00874e <gemv+0x48>
1c00870e: 00251e13 slli t3,a0,0x2
1c008712: 1e71 addi t3,t3,-4
1c008714: 00259e93 slli t4,a1,0x2
1c008718: 002e5e13 srli t3,t3,0x2
1c00871c: 01d68f33 add t5,a3,t4
1c008720: 0e05 addi t3,t3,1
1c008722: 015e407b lp.setup x0,t3,1c00874c <gemv+0x46>
1c008726: 40df07b3 sub a5,t5,a3
1c00872a: 17f1 addi a5,a5,-4
1c00872c: 0047258b p.lw a1,4(a4!) # 10004 <__l1_heap_size+0x20>
1c008730: 8389 srli a5,a5,0x2
1c008732: 8836 mv a6,a3
1c008734: 8532 mv a0,a2
1c008736: 0785 addi a5,a5,1
1c008738: 0087c0fb lp.setup x1,a5,1c008748 <gemv+0x42>
1c00873c: 0045230b p.lw t1,4(a0!)
1c008740: 0048288b p.lw a7,4(a6!)
1c008744: 431305b3 p.mac a1,t1,a7
1c008748: feb72e23 sw a1,-4(a4)
1c00874c: 9676 add a2,a2,t4
1c00874e: 8082 ret
// generic matrix-vector multiplication
void gemv(int size_N, int size_M,
float * mat_I, float *vec_i, float * vec_o)
{
for (int i=0; i<size_N; i++){
for (int j=0; j<size_M; j++){
// mulitply accumulate operation
vec_o[i] += mat_i[i*size_M+j] * vec_i[j];
}
}
}
APP = matrix-vector
APP_SRCS += test.c
APP_CFLAGS += -O3 -g -mnohwloops
APP_LDFLAGS +=
include $(RULES_DIR)/pmsis_rules.mk
Inner loop
Hardware Loops Instructions have been placed!

## Slide 24: Performance Counters: Measuring the CPU Time
Each RI5CY core provides a performance counter. These 32-bit counters can be configured to count the:
  Total number of cycles (also includes the cycles where the core is sleeping)
  Number of cycles the core was active (not sleeping)
  Number of instructions executed
  Number of load data hazards
  Number of jump register data hazards
  Number of cycles waiting for instruction fetches, i.e. number of instructions wasted due to non-ideal caching
  Number of data memory loads executed. Misaligned accesses are counted twice
  Number of data memory stores executed. Misaligned accesses are counted twice
  Number of unconditional jumps (j, jal, jr, jalr)
  Number of both taken and not taken branches
  Number of taken branches
  Number of compressed instructions executed
The performance counters of the cluster cores can also count the:
Number of memory loads to EXT executed. Misaligned accesses are counted twice. Every non-L1 access is considered external
Number of memory stores to EXT executed. Misaligned accesses are counted twice. Every non-L1 access is considered external
Number of cycles used for memory loads to EXT. Every non-L1 access is considered external
Number of cycles used for memory stores to EXT. Every non-L1 access is considered external
Number of cycles wasted due to L1/log-interconnect contention
RISC-V
Core
Performance Counters
Important: while on the PULP Virtual Platform multiple perf counters can be enabled concurrently, only one counter is available on a real HW device!

## Slide 25: Using the performance Counters on PULP
Using the PMSIS library APIs:
/rtos/pmsis/pmsis_api/include/pmsis/chips/default.h
// enable the perf counters of interest
pi_perf_conf( 1 << PI_PERF_CYCLES |
1 << PI_PERF_INSTR );
// reset the performance counters
pi_perf_reset();
// start the performance counters
pi_perf_start();
// task to profile
foo();
// stop the performance counters
pi_perf_stop();
// collect and print statistics
uint32_t instr_cnt = pi_perf_read(PI_PERF_INSTR);
uint32_t cycles_cnt = pi_perf_read(PI_PERF_CYCLES);
Configure which performance counters to enable!

## Slide 26: Profile the gemv
Make a new project by copying the matrix-vector gemv example into a new directory
$ cp -r matrix_vector/ matrix_vector_perf/
$ cd matrix_vector_perf/
For each of the previous compiler optimizations, measure the performance using the PMSIS performance counters and report:
number of clock cycles
number of instructions
CPI
compute the number of clock cycles and instructions per elementary operation.
  1 elementary operation := 1 Multiply-and-Accumulate

## Slide 27: Profile the gemv
Make a new project by copying the matrix-vector gemv example into a new folder
$ cp -r matrix_vector/ matrix_vector_perf/
$ cd matrix_vector_perf/
Solution:
pi_perf_conf(1<<PI_PERF_CYCLES | 1<<PI_PERF_INSTR);
pi_perf_reset();
pi_perf_start();
// call the matrix-vector fucntion
gemv(N, M, matrix, vector, output_vec);
pi_perf_stop();
uint32_t instr_cnt = pi_perf_read(PI_PERF_INSTR);
uint32_t cycles_cnt = pi_perf_read(PI_PERF_CYCLES);
printf("Num.Istr: %d Num.Cycles: %d \n", instr_cnt, cycles_cnt);
 | -01 | -03 | -03 HWLoops
Clock Cycles | 22891 | 20282 | 12987
Instr. | 15835 | 12780 | 10483
CPI | 1.48 | 1.58 | 1.23
Clk Cyc / MAC | 9.1 | 8.1 | 5.1
Instr / MAC | 6.1 | 5.1 | 4.1
#MAC = N x M = 50 x 50 = 2500

## Slide 28: Lab Assignment
Provide an implementation of:
1. the C function gemvt()that takes an integer (int32) matrix and an integer vector and computes the vector , where is the transpose of .
2. the C function gemm(), the general matrix multiply, that takes two NxN matrices and returns an NxN matrix.
For each function:
  Test the its correct behavior
  Measure the number of clock cycles, IPC and efficiency (MAC / clock cycles)
  Maximize efficiency!

## Slide 29
Alberto Dequino
Calin Diaconu
alberto.dequino@unibo.it
calin.diaconu2@unibo.it