## Slide 1: LAB04 Parallel programming on PULP with OpenMP
Andrea Belano andrea.belano2@unibo.it

## Slide 2: EXERCISE 1: Using the parallel construct and its data scope clauses
Add a parallel directive to execute all the printf calls on multiple cores NOTE: use the clause num_thread(NUM_CORES) to match the number of active cores in the execution environment with the CORES parameter in the make command.
What is the default data scope of a, b and c? Is this behavior correct?
Suppose to specify a private or firstprivate data scope for the a variable. Which behavior can be considered the correct one? Why?
$ git clone https://github.com/EEESlab/HSDES-LAB05-PULP_Parallel_OpenMP.git
$ cd HSDES-LAB05-PULP_Parallel_OpenMP
$ cd hello-omp
$ make clean all run CORES=1

## Slide 3: EXERCISE 2: Using the for construct
In "kernels.c," use a for directive with no additional clauses to parallelize the matrix multiplication kernel. Is the schedule static or dynamic? How is the workload distributed?
Modify the code to apply a static schedule with chunk size = 1. Compare its performance with the previous case.
Modify the code to apply a dynamic schedule. Compare its performance to that of the previous cases and explain the differences.
$ cd HSDES-LAB05-PULP_Parallel_OpenMP
$ cd matrixMul-omp
$ make clean all run CORES=1

## Slide 4: EXERCISE 3: Using critical sections and reductions
In “cluster.c”, parallelize the iterative_pi computation using a for directive (with no additional clauses). Is it a static or dynamic schedule? How is the workload distributed? Is the result correct when executing on 8 cores?
Modify the code to add a critical section for the area computation (area += value). Check the result when executing on 8 cores and compute the parallel speedup.
Modify the code to use a reduction clause instead of a critical section Compare the performance to that of the previous case and explain the differences.
$ cd HSDES-LAB05-PULP_Parallel_OpenMP
$ cd computePi-omp
$ make clean all run CORES=1

## Slide 5: EXERCISE 4: Task parallelism
In “cluster.c”, parallelize compute_functions considering each for loop as a separate task by using conditions on the thread id or using the sections directive.
Compute the parallel speedup.
[OPTIONAL] Compare this solution to an alternative one applying data parallelism inside each loop.
$ cd HSDES-LAB05-PULP_Parallel_OpenMP
$ cd computeTrigFunctions-omp
$ make clean all run CORES=1

## Slide 6: Lab Assignment
Compare all the previous exercises with their equivalent version using bare-metal parallelization.
Which solution is better?

## Slide 7: PULP OpenMP support
Add the following line to the Makefile: CONFIG_OPENMP = 1
Avoid explicit forks inside the cluster  the program execution starts on a single core, parallelism is expressed by means of OpenMP directives
Call rt_omp_start inside the cluster code before using any OpenMP directives and/or runtime functions
Use OpenMP directives and functions to express parallelism

## Slide 8: Reference on Makefile rules
The Makefile is a “recipe” used to call the compiler/linker and, in this case, also to run the program. You can also chain several rules (e.g., make clean all run) and pass options (e.g., runner_args="--vcd")
Remove any existing build
make clean
Build program (calling compiler + linker)
make all
Run the program
make run
Run options: you can change them by adding runner_args="OPTIONS"
make run runner_args="--trace=.*insn.*" > trace.log # written trace of instructions
Disassembling:
make dis > test.S # disassemble without inlined source code
/app/riscv-gcc/bin/riscv32-unknown-elf-objdump –D -S > test.S # disassemble with inlined source code

## Slide 9
Andrea Belano andrea.belano2@unibo.it